[Code of Federal Regulations]

[Title 49, Volume 2]

[Revised as of October 1, 2007]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR180.3]

[Page 1118-1119]

TITLE 49--TRANSPORTATION

CHAPTER I--PIPELINE AND HAZARDOUS MATERIALS SAFETY ADMINISTRATION,

DEPARTMENT OF TRANSPORTATION

PART 180_CONTINUING QUALIFICATION AND MAINTENANCE OF PACKAGINGS--Table

of Contents

Subpart A_General

Sec. 180.3  General requirements.

(a) No person may represent, mark, certify, sell, or offer a

packaging or container as meeting the requirements of this part, or a

special permit pertaining to this part issued under subchapter A of this

chapter, whether or not the packaging or container is intended to be

used for the transportation of a hazardous material, unless it is

marked, maintained, reconditioned, repaired, or retested, as

appropriate, in accordance with this part, an approval issued

thereunder, or a special permit issued under subchapter A of this

chapter.

(b) The representations, markings, and certifications subject to the

prohibitions of paragraph (a) of this section include:

(1) Identifications that include the letters ``DOT'', ``MC'',

``ICC'', or ``UN'';

(2) Special permit, approval, and registration numbers that include

the letters ``DOT'';

(3) Test dates displayed in association with specification,

registration, approval, or exemption markings indicating conformance to

a test or retest requirement of this subchapter, an approval issued

thereunder, or a special permit issued under subchapter A of this

chapter;

(4) Documents indicating conformance to the testing, inspection,

maintenance or other continuing qualification requirements of this part;

and

(5) Sales literature, including advertising, indicating that the

packaging

[[Page 1119]]

or container represented therein conforms to requirements contained in

subchapter A or C of this chapter.

[Amdt. 180-2, 54 FR 25032, June 12, 1989, as amended by Amdt. 180-3, 58

FR 33306, June 16, 1993; 70 FR 73166, Dec. 9, 2005]

Subpart B [Reserved]

[Code of Federal Regulations]

[Title 49, Volume 2]

[Revised as of October 1, 2007]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR180.205]

[Page 1120-1123]

TITLE 49--TRANSPORTATION

CHAPTER I--PIPELINE AND HAZARDOUS MATERIALS SAFETY ADMINISTRATION,

DEPARTMENT OF TRANSPORTATION

PART 180_CONTINUING QUALIFICATION AND MAINTENANCE OF PACKAGINGS--Table

of Contents

Subpart C_Qualification, Maintenance and Use of Cylinders

Sec. 180.205  General requirements for requalification of specification

cylinders.

(a) General. Each cylinder used for the transportation of hazardous

materials must be an authorized packaging. To qualify as an authorized

packaging, each cylinder must conform to this subpart, the applicable

requirements specified in part 173 of this subchapter, and the

applicable requirements of subpart C of part 178 of this subchapter.

(b) Persons performing requalification functions. No person may

represent that a repair or requalification of a cylinder has been

performed in accordance with the requirements in this subchapter unless

that person holds a current approval issued under the procedural

requirements prescribed in subpart I of part 107 of this chapter. No

person may mark a cylinder with a RIN and a requalification date or

otherwise represent that a DOT specification or special permit cylinder

has been requalified unless all applicable requirements of this subpart

have been met. A person who requalifies cylinders must maintain the

records prescribed in Sec.180.215 at each location at which it

inspects, tests, or marks cylinders.

(c) Periodic requalification of cylinders. Each cylinder bearing a

DOT specification marking must be requalified and marked as specified in

the Requalification Table in this subpart. Each cylinder bearing a DOT

special permit number must be requalified and marked in conformance with

this section and the terms of the applicable special permit. No cylinder

may be filled with a hazardous material and offered for transportation

in commerce unless that cylinder has been successfully requalified and

marked in accordance with this subpart. A cylinder may be requalified at

any time during or before the month and year that the requalification is

due. However, a cylinder filled before the requalification becomes due

may remain in service until it is emptied. A cylinder with a specified

service life may not be refilled and offered for transportation after

its authorized service life has expired.

(1) Each cylinder that is requalified in accordance with the

requirements specified in this section must be marked in accordance with

Sec.180.213.

(2) Each cylinder that fails requalification must be:

(i) Rejected and may be repaired or rebuilt in accordance with Sec.

180.211 or Sec.180.212, as appropriate; or

(ii) Condemned in accordance with paragraph (i) of this section.

(3) For DOT specification cylinders, the marked service pressure may

be changed upon approval of the Associate Administrator and in

accordance with written procedures specified in the approval.

(4) For a specification 3, 3A, 3AA, 3AL, 3AX, 3AXX, 3B, 3BN, or 3T

cylinder filled with gases in other than Division 2.2, from the first

requalification due on or after December 31, 2003, the burst pressure of

a CG-1, CG-4, or CG-5 pressure relief device must be at test pressure

with a tolerance of plus zero to minus 10%. An additional 5% tolerance

is allowed when a combined rupture disc is placed inside a holder. This

requirement does not apply if a CG-2, CG-3 or CG-9 thermally activated

relief device or a CG-7 reclosing pressure valve is used on the

cylinder.

(d) Conditions requiring test and inspection of cylinders. Without

regard to any other periodic requalification requirements, a cylinder

must be tested and inspected in accordance with this section prior to

further use if--

(1) The cylinder shows evidence of dents, corrosion, cracked or

abraded areas, leakage, thermal damage, or any other condition that

might render it unsafe for use in transportation;

[[Page 1121]]

(2) The cylinder has been in an accident and has been damaged to an

extent that may adversely affect its lading retention capability;

(3) The cylinder shows evidence of or is known to have been over-

heated; or

(4) The Associate Administrator determines that the cylinder may be

in an unsafe condition.

(e) Cylinders containing Class 8 (corrosive) liquids. A cylinder

previously containing a Class 8 (corrosive) liquid may not be used to

transport a Class 2 material in commerce unless the cylinder is--

(1) Visually inspected, internally and externally, in accordance

with paragraph (f) of this section and the inspection is recorded as

prescribed in Sec.180.215;

(2) Requalified in accordance with this section, regardless of the

date of the previous requalification;

(3) Marked in accordance with Sec.180.213; and

(4) Decontaminated to remove all significant residue or impregnation

of the Class 8 material.

(f) Visual inspection. Except as otherwise provided in this subpart,

each time a cylinder is pressure tested, it must be given an internal

and external visual inspection.

(1) The visual inspection must be performed in accordance with the

following CGA Pamphlets: C-6 for steel and nickel cylinders (IBR, see

Sec.171.7 of this subchapter); C-6.1 for seamless aluminum cylinders

(IBR, see Sec.171.7 of this subchapter); C-6.2 for fiber reinforced

composite special permit cylinders (IBR, see Sec.171.7 of this

subchapter); C-6.3 for low pressure aluminum cylinders (IBR, see Sec.

171.7 of this subchapter); C-8 for DOT 3HT cylinders (IBR, see Sec.

171.7 of this subchapter); and C-13 for DOT 8 series cylinders (IBR, see

Sec.171.7 of this subchapter).

(2) For each cylinder with a coating or attachments that would

inhibit inspection of the cylinder, the coating or attachments must be

removed before performing the visual inspection.

(3) Each cylinder subject to visual inspection must be approved,

rejected, or condemned according to the criteria in the applicable CGA

pamphlet.

(4) In addition to other requirements prescribed in this paragraph

(f), each specification cylinder manufactured of aluminum alloy 6351-T6

and used in self-contained underwater breathing apparatus (SCUBA), self-

contained breathing apparatus (SCBA), or oxygen service must be

inspected for sustained load cracking in accordance with Appendix C of

this part at the first scheduled 5-year requalification period after

January 1, 2007, and every five years thereafter.

(g) Pressure test. (1) Unless otherwise provided, each cylinder

required to be retested under this subpart must be retested by means

suitable for measuring the expansion of the cylinder under pressure.

Bands and other removable attachments must be loosened or removed before

testing so that the cylinder is free to expand in all directions.

(2) The pressure indicating device of the testing apparatus must

permit reading of pressures to within 1% of the minimum prescribed test

pressure of each cylinder tested, except that for an analog device,

interpolation to \1/2\ of the marked gauge divisions is acceptable. The

expansion-indicating device of the testing apparatus must also permit

incremental reading of the cylinder expansion to 1% of the total

expansion of each cylinder tested or 0.1 cc, whichever is larger.

Midpoint visual interpolation is permitted.

(3) Each day before retesting, the retester shall confirm, by using

a calibrated cylinder or other method authorized in writing by the

Associate Administrator, that:

(i) The pressure-indicating device, as part of the retest apparatus,

is accurate within <plus-minus<ls-thn-eq>1.0% of the prescribed test

pressure of any cylinder tested that day. The pressure indicating

device, itself, must be certified as having an accuracy of <plus-

minus<ls-thn-eq>0.5%, or better, of its full range, and must permit

readings of pressure from 90%-110% of the minimum prescribed test

pressure of the cylinder to be tested. The accuracy of the pressure

indicating device within the test system can be demonstrated at any

point within 500 psig of the actual test pressure for test pressures at

or above 3000 psig, or 10% of the actual test pressure for test

pressures below 3000 psig.

[[Page 1122]]

(ii) The expansion-indicating device, as part of the retest

apparatus, gives a stable reading of expansion and is accurate to <plus-

minus<ls-thn-eq>1.0% of the total expansion of any cylinder tested or

0.1 cc, whichever is larger. The expansion-indicating device itself must

have an accuracy of <plus-minus<ls-thn-eq>0.5%, or better, of its full

scale.

(4) The test equipment must be verified to be accurate within <plus-

minus<ls-thn-eq>1.0% of the calibrated cylinder's pressure and

corresponding expansion values. This may be accomplished by bringing the

pressure to a value shown on the calibration certificate for the

calibrated cylinder used and verifying that the resulting total

expansion is within <plus-minus<ls-thn-eq>1.0% of the total expansion

shown on the calibration certificate. Alternatively, calibration may be

demonstrated by bringing the total expansion to a known value on the

calibration certificate for the calibrated cylinder used and verifying

that the resulting pressure is within <plus-minus<ls-thn-eq>1.0% of the

pressure shown on the calibration certificate. The calibrated cylinder

must show no permanent expansion. The retester must demonstrate

calibration in conformance with this paragraph (g) to an authorized

inspector on any day that it retests cylinders. A retester must maintain

calibrated cylinder certificates in conformance with Sec.

180.215(b)(4).

(5) Minimum test pressure must be maintained for at least 30

seconds, and as long as necessary for complete expansion of the

cylinder. A system check may be performed at or below 90% of test

pressure prior to the retest. In the case of a malfunction of the test

equipment, the test may be repeated at a pressure increased by 10% or

100 psig, whichever is less. This paragraph (g) does not authorize

retest of a cylinder otherwise required to be condemned under paragraph

(i) of this section.

(h) Cylinder rejection. A cylinder must be rejected when, after a

visual inspection, it meets a condition for rejection under the visual

inspection requirements of paragraph (f) of this section.

(1) Except as provided in paragraphs (h)(3) and (h)(4) of this

section, a cylinder that is rejected may not be marked as meeting the

requirements of this section.

(2) The requalifier must notify the cylinder owner, in writing, that

the cylinder has been rejected.

(3) Unless the cylinder is requalified in conformance with

requirements in Sec.180.211, it may not be filled with a hazardous

material and offered for transportation in commerce where use of a

specification packaging is required.

(4) A rejected cylinder with a service pressure of less than 900

psig may be requalified and marked if the cylinder is repaired or

rebuilt and subsequently inspected and tested in conformance with--

(i) The visual inspection requirements of paragraph (f) of this

section;

(ii) Part 178 of this subchapter and this part;

(iii) Any special permit covering the manufacture, requalification,

and/or use of that cylinder; and

(iv) Any approval required under Sec.180.211.

(i) Cylinder condemnation. (1) A cylinder must be condemned when--

(i) The cylinder meets a condition for condemnation under the visual

inspection requirements of paragraph (f) of this section.

(ii) The cylinder leaks through its wall.

(iii) Evidence of cracking exists to the extent that the cylinder is

likely to be weakened appreciably.

(iv) For a DOT specification cylinder, other than a DOT 4E aluminum

cylinder or a special permit cylinder, permanent expansion exceeds 10

percent of total expansion.

(v) For a DOT 3HT cylinder--

(A) The pressure test yields an elastic expansion exceeding the

marked rejection elastic expansion (REE) value.

(B) The cylinder shows evidence of denting or bulging.

(C) The cylinder bears a manufacture or an original test date older

than twenty-four years or after 4380 pressurizations, whichever occurs

first. If a cylinder is refilled, on average, more than once every other

day, an accurate record of the number of rechargings must be maintained

by the cylinder owner or the owner's agent.

(vi) For a DOT 4E aluminum cylinder, permanent expansion exceeds 12

percent of total expansion.

[[Page 1123]]

(vii) For a DOT special permit cylinder, permanent expansion exceeds

the limit in the applicable special permit, or the cylinder meets

another criterion for condemnation in the applicable special permit.

(viii) For an aluminum or an aluminum-lined composite special permit

cylinder, the cylinder is known to have been or shows evidence of having

been over-heated.

(2) When a cylinder must be condemned, the requalifier must--

(i) Stamp a series of X's over the DOT specification number and the

marked pressure or stamp ``CONDEMNED'' on the shoulder, top head, or

neck using a steel stamp;

(ii) For composite cylinders, securely affix to the cylinder a label

with the word ``CONDEMNED'' overcoated with epoxy near, but not

obscuring, the original cylinder manufacturer's label; or

(iii) As an alternative to the stamping or labeling as described in

this paragraph (i)(2), at the direction of the owner, the requalifier

may render the cylinder incapable of holding pressure.

(3) No person may remove or obliterate the ``CONDEMNED'' marking. In

addition, the requalifier must notify the cylinder owner, in writing,

that the cylinder is condemned and may not be filled with hazardous

material and offered for transportation in commerce where use of a

specification packaging is required.

[67 FR 51660, Aug. 8, 2002, as amended at 68 FR 24662, May 8, 2003; 68

FR 75764, Dec. 31, 2003; 70 FR 34077, June 13, 2005; 70 FR 73166, Dec.

9, 2005; 71 FR 51128, Aug. 29, 2006]

[Code of Federal Regulations]

[Title 49, Volume 2]

[Revised as of October 1, 2007]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR180.209]

[Page 1124-1128]

TITLE 49--TRANSPORTATION

CHAPTER I--PIPELINE AND HAZARDOUS MATERIALS SAFETY ADMINISTRATION,

DEPARTMENT OF TRANSPORTATION

PART 180_CONTINUING QUALIFICATION AND MAINTENANCE OF PACKAGINGS--Table

of Contents

Subpart C_Qualification, Maintenance and Use of Cylinders

Sec. 180.209  Requirements for requalification of specification

cylinders.

(a) Periodic qualification of cylinders. (1) Each specification

cylinder that becomes due for periodic requalification, as specified in

the following table, must be requalified and marked in conformance with

the requirements of this subpart. Requalification records must be

maintained in accordance with Sec.180.215. Table 1 follows:

Table 1--Requalification of Cylinders \1\

------------------------------------------------------------------------

Specification under which       Minimum test         Requalification

cylinder was made       pressure  (psig) \2\     period  (years)

------------------------------------------------------------------------

DOT 3.......................  3000 psig...........  5

DOT 3A, 3AA.................  5/3 times service     5, 10, or 12 (see

pressure, except      Sec.180.209(b),

noncorrosive          (f), (h), and (j)

service (see Sec.

180.209(g)).

DOT 3AL.....................  5/3 times service     5 or 12 (see Sec.

pressure.             180.209(j) and Sec.

180.209(m) \3\ ).

DOT 3AX, 3AAX...............  5/3 times service     5

pressure.

3B, 3BN.....................  2 times service       5 or 10 (see Sec.

pressure (see Sec.180.209(f))

180.209(g)).

3E..........................  Test not required...

3HT.........................  5/3 times service     3 (see Sec.Sec.

pressure.             180.209(k) and

180.213(c))

3T..........................  5/3 times service     5

pressure.

4AA480......................  2 times service       5 or 10 (see Sec.

pressure (see Sec.180.209(h))

180.209(g)).

4B, 4BA, 4BW, 4B-240ET......  2 times service       5, 10, or 12 (see

pressure, except      Sec.180.209(e),

non-corrosive         (f), and (j))

service (see Sec.

180.209(g)).

4D, 4DA, 4DS................  2 times service.....  5

[[Page 1125]]

DOT 4E......................  2 times service       5

pressure, except

non-corrosive (see

Sec.180.209(g)).

4L..........................  Test not required...

8, 8AL......................  ....................  10 or 20 (see Sec.

180.209(i))

Exemption or special permit   See current           See current

cylinder.                     exemption or          exemption or

special permit.       special permit

Foreign cylinder (see Sec.As marked on          5 (see Sec.Sec.

173.301(j) of this            cylinder, but not     180.209(l) and

subchapter for restrictions   less than 5/3 of      180.213(d)(2))

on use).                      any service or

working pressure

marking.

------------------------------------------------------------------------

\1\ Any cylinder not exceeding 2 inches outside diameter and less than 2

feet in length is excepted from volumetric expansion test.

\2\ For cylinders not marked with a service pressure, see Sec.

173.301a(b) of this subchapter.

(b) DOT 3A or 3AA cylinders. (1) A cylinder conforming to

specification DOT 3A or 3AA with a water capacity of 56.7 kg (125 lb) or

less that is removed from any cluster, bank, group, rack, or vehicle

each time it is filled, may be requalified every ten years instead of

every five years, provided the cylinder conforms to all of the following

conditions:

(i) The cylinder was manufactured after December 31, 1945.

(ii) The cylinder is used exclusively for air; argon; cyclopropane;

ethylene; helium; hydrogen; krypton; neon; nitrogen; nitrous oxide;

oxygen; sulfur hexafluoride; xenon; chlorinated hydrocarbons,

fluorinated hydrocarbons, liquefied hydrocarbons, and mixtures thereof

that are commercially free from corroding components; permitted mixtures

of these gases (see Sec.173.301(d) of this subchapter); and permitted

mixtures of these gases with up to 30 percent by volume of carbon

dioxide, provided the gas has a dew point at or below minus (52 [deg]F)

at 1 atmosphere.

(iii) Before each refill, the cylinder is removed from any cluster,

bank, group, rack or vehicle and passes the hammer test specified in CGA

Pamphlet C-6 (IBR, see Sec.171.7 of this subchapter).

(iv) The cylinder is dried immediately after hydrostatic testing to

remove all traces of water.

(v) The cylinder is not used for underwater breathing.

(vi) Each cylinder is stamped with a five-pointed star at least one-

fourth of an inch high immediately following the test date.

(2) If, since the last required requalification, a cylinder has not

been used exclusively for the gases specifically identified in paragraph

(b)(1)(ii) of this section, but currently conforms with all other

provisions of paragraph (b)(1) of this section, it may be requalified

every 10 years instead of every five years, provided it is first

requalified and examined as prescribed by Sec.173.302a(b) (2), (3) and

(4) of this subchapter.

(3) Except as specified in paragraph (b)(2) of this section, if a

cylinder, marked with a star, is filled with a compressed gas other than

as specified in paragraph (b)(1)(ii) of this section, the star following

the most recent test date must be obliterated. The cylinder must be

requalified five years from the marked test date, or prior to the first

filling with a compressed gas, if the required five-year requalification

period has passed.

(c) DOT 4-series cylinders. A DOT 4-series cylinder, except a 4L

cylinder, that at any time shows evidence of a leak or of internal or

external corrosion, denting, bulging or rough usage to the extent that

it is likely to be weakened appreciably, or that has lost five percent

or more of its official tare weight must be requalified before being

refilled and offered for transportation. (Refer to CGA Pamphlet C-6 or

C-6.3, as applicable, regarding cylinder weakening.) After testing, the

actual tare weight must be recorded as the new tare weight.

(d) Cylinders 5.44 kg (12 lb) or less with service pressures of 300

psig or less. A cylinder of 5.44 (12 lb) or less water capacity

authorized for service pressure of 300 psig or less must be given a

complete external visual inspection at the time periodic requalification

becomes due. External visual inspection must be

[[Page 1126]]

in accordance with CGA Pamphlet C-6 or C-6.1 (IBR, see Sec.171.7 of

this subchapter). The cylinder may be proof pressure tested. The test is

successful if the cylinder, when examined under test pressure, does not

display a defect described in Sec.180.205(i)(1) (ii) or (iii). Upon

successful completion of the test and inspection, the cylinder must be

marked in accordance with Sec.180.213.

(e) Proof pressure test A cylinder made in conformance with

specifications DOT 4B, 4BA, 4BW, or 4E used exclusively for: liquefied

petroleum gas that meets the detail requirement limits in Table I of

ASTM D 1835, ``Standard Specification for Liquefied Petroleum (LP)

Gases'' (IBR see Sec.171.7 of this subchapter) or an equivalent

standard containing the same limits; anhydrous dimethylamine; anhydrous

methylamine; anhydrous trimethylamine; methyl chloride; methylacetylene-

propadiene stabilized; or dichlorodifluoromethane, difluoroethane,

difluorochloroethane, chlorodifluoromethane, chlorotetrafluoroethane,

trifluorochloroethylene, or mixture thereof, or mixtures of one or more

with trichlorofluoromethane; and commercially free from corroding

components and protected externally by a suitable corrosion-resistant

coating (such as galvanizing or painting) may be requalified by

volumetric expansion testing every 12 years instead of every five years.

As an alternative, the cylinder may be subjected to a proof pressure

test at least two times the marked service pressure, but this latter

type of test must be repeated every seven years after expiration of the

first 12-year period. When subjected to a proof pressure test, the

cylinder must be carefully examined under test pressure and removed from

service if a leak or defect is found.

(f) Poisonous materials. A cylinder conforming to specification DOT

3A, 3AA, 3B, 4BA, or 4BW having a service pressure of 300 psig or less

and used exclusively for methyl bromide, liquid; mixtures of methyl

bromide and ethylene dibromide, liquid; mixtures of methyl bromide and

chlorpicrin, liquid; mixtures of methyl bromide and petroleum solvents,

liquid; or methyl bromide and nonflammable, nonliquefied compressed gas

mixtures, liquid; commercially free of corroding components, and

protected externally by a suitable corrosion resistant coating (such as

galvanizing or painting) and internally by a suitable corrosion

resistant lining (such as galvanizing) may be tested every 10 years

instead of every five years, provided a visual internal and external

examination of the cylinder is conducted every five years in accordance

with CGA Pamphlet C-6. The cylinder must be examined at each filling,

and rejected if a dent, corroded area, leak or other condition indicates

possible weakness.

(g) Visual inspections. A cylinder conforming to a specification

listed in the table in this paragraph and used exclusively in the

service indicated may, instead of a periodic hydrostatic test, be given

a complete external visual inspection at the time periodic

requalification becomes due. External visual inspection must be in

accordance with CGA Pamphlet C-6 or C-6.3, as applicable (IBR, see Sec.

171.7 of this subchapter). When this inspection is used instead of

hydrostatic pressure testing, subsequent inspections are required at

five-year intervals after the first inspection. After May 31, 2004,

inspections must be made only by persons holding a current RIN and the

results recorded and maintained in accordance with Sec.180.215.

Records must include: date of inspection (month and year); DOT

specification number; cylinder identification (registered symbol and

serial number, date of manufacture, and owner); type of cylinder

protective coating (including statement as to need of refinishing or

recoating); conditions checked (e.g., leakage, corrosion, gouges, dents

or digs in shell or heads, broken or damaged footring or protective ring

or fire damage); disposition of cylinder (returned to service, returned

to cylinder manufacturer for repairs or condemned). A cylinder passing

requalification by the external visual inspection must be marked in

accordance with Sec.180.213. Specification cylinders must be in

exclusive service as shown in the following table:

[[Page 1127]]

------------------------------------------------------------------------

Cylinders conforming to--              Used exclusively for--

------------------------------------------------------------------------

DOT 3A, DOT 3AA, DOT 3A480X, DOT 4AA480  Anhydrous ammonia of at least

99.95% purity.

DOT 3A, DOT 3AA, DOT 3A480X, DOT 3B,     Butadiene, inhibited, that is

DOT 4B, DOT 4BA, DOT 4BW.                commercially free from

corroding components.

DOT 3A, DOT 3A480X, DOT 3AA, DOT 3B,     Cyclopropane that is

DOT 4AA480, DOT 4B, DOT 4BA, DOT 4BW.    commercially free from

corroding components.

DOT 3A, DOT 3AA, DOT 3A480X, DOT 4B,     Chlorinated hydrocarbons and

DOT 4BA, DOT 4BW, DOT 4E.                mixtures thereof that are

commercially free from

corroding components.

DOT 3A, DOT 3AA, DOT 3A480X, DOT 4B,     Fluorinated hydrocarbons and

DOT 4BA, DOT 4BW, DOT 4E.                mixtures thereof that are

commercially free from

corroding components.

DOT 3A, DOT 3AA, DOT 3A480X, DOT 3B,     Liquefied hydrocarbon gas that

DOT 4B, DOT 4BA, DOT 4BW, DOT 4E.        is commercially free from

corroding components.

DOT 3A, DOT 3AA, DOT 3A480X, DOT 3B,     Liquefied petroleum gas that

DOT 4B, DOT 4BA, DOT 4BW, DOT 4E.        meets the detail requirements

limits in Table 1 of ASTM

1835, Standard Specification

for Liquefied Petroleum (LP)

Gases (incorporated by

reference; see Sec.171.7 of

this subchapter) or an

equivalent standard containing

the same limits.

DOT 3A, DOT 3AA, DOT 3B, DOT 4B, DOT     Methylacetylene-propadiene,

4BA, DOT 4BW, DOT 4E.                    stabilized, that is

commercially free from

corroding components.

DOT 3A, DOT 3AA, DOT 3B, DOT 4B, DOT     Anhydrous mono,

4BA, DOT 4BW.                            di,trimethylamines that are

commercially free from

corroding components.

DOT 4B240, DOT 4BW240..................  Ethyleneimine, stabilized.

------------------------------------------------------------------------

(h) Cylinders containing anhydrous ammonia. A cylinder conforming to

specification DOT 3A, 3A480X, or 4AA480 used exclusively for anhydrous

ammonia, commercially free from corroding components, and protected

externally by a suitable corrosion-resistant coating (such as paint) may

be requalified every 10 years instead of every five years.

(i) Requalification of DOT-8 series cylinders. (1) Each owner of a

DOT-8 series cylinder used to transport acetylene must have the cylinder

shell and the porous filler requalified in accordance with CGA Pamphlet

C-13 (IBR, see Sec.171.7 of this subchapter). Requalification must be

performed in accordance with the following schedule:

----------------------------------------------------------------------------------------------------------------

Shell (visual inspection)             Porous filler requalification

requalification            ---------------------------------------

Date of cylinder manufacture   ----------------------------------------

Initial           Subsequent            Intial            Subsequent

----------------------------------------------------------------------------------------------------------------

Before January 1, 1991..........  Before January 1,   10 years..........  Before January 1,   Not required.

2001.                                   2011.

On or after January 1, 1991.....  10 years \1\......  10 years..........  5 to 20 years \2\.  Not required.

----------------------------------------------------------------------------------------------------------------

\1\ Years from the date of cylinder manufacture.

\2\ No sooner than 5 years, and no later than 20 years from the date of manufacture.

(2) Unless requalified and marked in accordance with CGA Pamphlet C-

13 before October 1, 1994, an acetylene cylinder must be requalified by

a person who holds a current RIN.

(3) If a cylinder valve is replaced, a cylinder valve of the same

weight must be used or the tare weight of the cylinder must be adjusted

to compensate for valve weight differential.

(4) The person performing a visual inspection or requalification

must record the results as specified in Sec.180.215.

(5) The person performing a visual inspection or requalification

must mark the cylinder as specified in Sec.180.213.

(j) Cylinder used as a fire extinguisher. Only a DOT specification

cylinder used as a fire extinguisher and meeting Special Provision 18 in

Sec.172.102(c)(1) of this subchapter may be requalified in accordance

with this paragraph (j).

(1) A DOT 4B, 4BA, 4B240ET or 4BW cylinder may be tested as follows:

(i) For a cylinder with a water capacity of 5.44 kg (12 lb) or less,

by volumetric expansion test using the water jacket method or by proof

pressure test. A requalification must be performed by the end of 12

years after the original test date and at 12-year intervals thereafter.

(ii) For a cylinder having a water capacity over 5.44 kg (12 lb)--

(A) By proof pressure test. A requalification must be performed by

the end of 12 years after the original test date and at 7-year

intervals; or

[[Page 1128]]

(B) By volumetric expansion test using the water jacket method. A

requalification must be performed 12 years after the original test date

and at 12-year intervals thereafter.

(2) A DOT 3A, 3AA, or 3AL cylinder must be requalified by volumetric

expansion test using the water jacket method. A requalification must be

performed 12 years after the original test date and at 12-year intervals

thereafter.

(k) 3HT cylinders. In addition to the other requirements of this

section, a cylinder marked DOT-3HT must be requalified in accordance

with CGA C-8 (IBR, see Sec.171.7 of this subchapter).

(l) Requalification of foreign cylinders filled for export. A

cylinder manufactured outside the United States, other than as provided

in Sec.171.12a of this subchapter, that has not been manufactured,

inspected, tested and marked in accordance with part 178 of this

subchapter may be filled with compressed gas in the United States, and

shipped solely for export if it meets the following requirements, in

addition to other requirements of this subchapter:

(1) It has been inspected, tested and marked (with only the month

and year of test) in conformance with the procedures and requirements of

this subpart or the Associate Administrator has authorized the filling

company to fill foreign cylinders under an alternative method of

qualification; and

(2) It is offered for transportation in conformance with the

requirements of Sec.173.301(l) of this subchapter.

(m) DOT-3AL cylinders manufactured of 6351-T6 aluminum alloy. In

addition to the periodic requalification and marking described in Sec.

180.205, each cylinder manufactured of aluminum alloy 6351-T6 used in

self-contained underwater breathing apparatus (SCUBA), self-contained

breathing apparatus (SCBA), or oxygen service must be requalified and

inspected for sustained load cracking in accordance with the non-

destructive examination method described in the following table. Each

cylinder with sustained load cracking that has expanded into the neck

threads must be condemned in accordance with Sec.180.205(i). This

provision does not apply to cylinders used for carbon dioxide, fire

extinguisher or other industrial gas service.

Requalification and Inspection of DOT-3AL Cylinders Made of Aluminum Alloy 6351-T6

----------------------------------------------------------------------------------------------------------------

Sustained Load Cracking   Requalification

Requalification requirement         Examination procedure \1\   Condemnation Criteria \2\   period (years)

----------------------------------------------------------------------------------------------------------------

Eddy current examination combined with   Eddy current--In            Any crack in the neck or                5

visual inspection.                       accordance with Appendix    shoulder of 2 thread

C of this part.             lengths or more.

Visual inspection--In

accordance with CGA

Pamphlet C-6.1 (IBR; see

Sec.171.7 of this

subchapter).

----------------------------------------------------------------------------------------------------------------

\1\ The requalifier performing eddy current must be familiar with the eddy current equipment and must

standardize (calibrate) the system in accordance with the requirements provided in Appendix C to this part.

\2\ The eddy current must be applied from the inside of the cylinder's neck to detect any sustained load

cracking that has expanded into the neck threads.

[67 FR 51660, Aug. 8, 2002, as amended at 68 FR 24662, May 8, 2003; 68

FR 55544, Sept. 26, 2003; 68 FR 48572, Aug. 14, 2003; 68 FR 75764, Dec.

31, 2003; 70 FR 73166, Dec. 9, 2005; 71 FR 51128, Aug. 29, 2005; 72 FR

55696, Oct. 1, 2007]

Editorial Note: The following amendment could not be incorporated

into Sec.180.209 because of the inaccurate amendatory instruction. For

the convenience of the user the amendatory instruction and text is set

forth as follows:

At 71 FR 54397, Sept. 14, 2006, Sec.180.209 was amended in

paragraph (a)(1), the first and third entries in Table 1 were revised to

read as follows:

[Code of Federal Regulations]

[Title 49, Volume 2]

[Revised as of October 1, 2007]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR180.213]

[Page 1131-1133]

TITLE 49--TRANSPORTATION

CHAPTER I--PIPELINE AND HAZARDOUS MATERIALS SAFETY ADMINISTRATION,

DEPARTMENT OF TRANSPORTATION

PART 180_CONTINUING QUALIFICATION AND MAINTENANCE OF PACKAGINGS--Table

of Contents

Subpart C_Qualification, Maintenance and Use of Cylinders

Sec. 180.213  Requalification markings.

(a) General. Each cylinder or UN pressure receptacle requalified in

accordance with this subpart with acceptable results must be marked as

specified in this section. Required specification markings may not be

altered or removed.

(b) Placement of markings. Each cylinder must be plainly and

permanently marked on the metal of the cylinder as permitted by the

applicable specification. Unless authorized by the cylinder

specification, marking on the cylinder sidewall is prohibited.

(1) Requalification and required specification markings must be

legible so as to be readily visible at all times. Illegible

specification markings may be remarked on the cylinder as provided by

the original specification. Requalification markings may be placed on

[[Page 1132]]

any portion of the upper end of the cylinder excluding the sidewall, as

provided in this section. Requalification and required specification

markings that are illegible may be reproduced on a metal plate and

attached as provided by the original specification.

(2) Previous requalification markings may not be obliterated, except

that, when the space originally provided for requalification dates

becomes filled, additional dates may be added as follows:

(i) All preceding requalification dates may be removed by peening

provided that--

(A) Permission is obtained from the cylinder owner;

(B) The minimum wall thickness is maintained in accordance with

manufacturing specifications for the cylinder; and

(C) The original manufacturing test date is not removed.

(ii) When the cylinder is fitted with a footring, additional dates

may be marked on the external surface of the footring.

(c) Requalification marking method. The depth of requalification

markings may not be greater than specified in the applicable

specification. The markings must be made by stamping, engraving,

scribing or other method that produces a legible, durable mark.

(1) A cylinder used as a fire extinguisher (Sec.180.209(j)) may be

marked by using a pressure sensitive label.

(2) For a DOT 3HT cylinder, the test date and RIN must be applied by

low-stress steel stamps to a depth no greater than that prescribed at

the time of manufacture. Stamping on the sidewall is not authorized.

(3) For a composite cylinder, the requalification markings must be

applied on a pressure sensitive label, securely affixed in a manner

prescribed by the cylinder manufacturer, near the original

manufacturer's label. Stamping of the composite surface is not

authorized.

(d) Requalification markings. Each cylinder successfully passing

requalification must be marked with the RIN set in a square pattern,

between the month and year of the requalification date. The first

character of the RIN must appear in the upper left corner of the square

pattern; the second in the upper right; the third in the lower right;

and the fourth in the lower left. Example: A cylinder requalified in

September 2006, and approved by a person who has been issued RIN

``A123'', would be marked plainly and permanently into the metal of the

cylinder in accordance with location requirements of the cylinder

specification or on a metal plate permanently secured to the cylinder in

accordance with paragraph (b) of this section. An example of the

markings prescribed in this paragraph (d) is as follows:

A1

9 06 X

32

Where:

``9'' is the month of requalification

``A123'' is the RIN

``06'' is the year of requalification, and

``X'' represents the symbols described in paragraphs (f)(2) through

(f)(8) of this section.

(1) Upon written request, variation from the marking requirement may

be approved by the Associate Administrator.

(2) Exception. A cylinder subject to the requirements of Sec.

173.301(l) of this subchapter may not be marked with a RIN.

(e) Size of markings. The size of the markings must be at least 6.35

mm (\1/4\ in.) high, except RIN characters must be at least 3.18 mm (\1/

8\ in.) high.

(f) Marking illustrations. Examples of required requalification

markings for DOT specification and special permit cylinders are

illustrated as follows:

(1) For designation of the 5-year volumetric expansion test, 10-year

volumetric expansion test for UN cylinders and cylinders conforming to

Sec.180.209(f) and (h), or 12-year volumetric expansion test for fire

extinguishers conforming to Sec.173.309(b) of this subchapter and

cylinders conforming to Sec.180.209(e) and 180.209(g), the marking is

as illustrated in paragraph (d) of this section.

(2) For designation of the 10-year volumetric expansion test for

cylinders conforming to Sec.180.209(b), the marking is as illustrated

in paragraph (d) of this

[[Page 1133]]

section, except that the ``X'' is replaced with a five-point star.

(3) For designation of special filling limits up to 10% in excess of

the marked service pressure for cylinders conforming to Sec.

173.302a(b) of this subchapter, the marking is as illustrated in

paragraph (d) of this section, except that the ``X'' is replaced with a

plus sign ``+''.

(4) For designation of the proof pressure test, the marking is as

illustrated in paragraph (d) of this section, except that the ``X'' is

replaced with the letter ``S''.

(5) For designation of the 5-year external visual inspection for

cylinders conforming to Sec.180.209(g), the marking is as illustrated

in paragraph (d) of this section, except that the ``X'' is replaced with

the letter ``E''.

(6) For designation of DOT 8 series cylinder shell requalification

only, the marking is as illustrated in paragraph (d) of this section,

except that the ``X'' is replaced with the letter ``S''.

(7) For designation of DOT 8 series and UN cylinder shell and porous

filler requalification, the marking is as illustrated in paragraph (d)

of this section, except that the ``X'' is replaced with the letters

``FS.''

(8) For designation of a nondestructive examination combined with a

visual inspection, the marking is as illustrated in paragraph (d) of

this section, except that the ``X'' is replaced with the type of test

performed, for example the letters ``AE'' for acoustic emission or

``UE'' for ultrasonic examination.

(9) For designation of the eddy current examination combined with a

visual inspection, the marking is as illustrated in paragraph (d) of

this section, except the ``X'' is replaced with the letters ``VE.''

[67 FR 51660, Aug. 8, 2002, as amended at 70 FR 73166, Dec. 9, 2005; 71

FR 33896, June 12, 2006; 71 FR 51128, Aug. 29, 2006; 71 FR 78635, Dec.

29, 2006]

[Code of Federal Regulations]

[Title 49, Volume 2]

[Revised as of October 1, 2007]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR180.215]

[Page 1133-1134]

TITLE 49--TRANSPORTATION

CHAPTER I--PIPELINE AND HAZARDOUS MATERIALS SAFETY ADMINISTRATION,

DEPARTMENT OF TRANSPORTATION

PART 180_CONTINUING QUALIFICATION AND MAINTENANCE OF PACKAGINGS--Table

of Contents

Subpart C_Qualification, Maintenance and Use of Cylinders

Sec. 180.215  Reporting and record retention requirements.

(a) Facility records. A person who requalifies, repairs or rebuilds

cylinders must maintain the following records where the requalification

is performed:

(1) Current RIN issuance letter;

(2) If the RIN has expired and renewal is pending, a copy of the

renewal request;

(3) Copies of notifications to Associate Administrator required

under Sec.107.805 of this chapter;

(4) Current copies of those portions of this subchapter applicable

to its cylinder requalification and marking activities at that location;

(5) Current copies of all special permits governing exemption

cylinders requalified or marked by the requalifier at that location; and

(6) The information contained in each applicable CGA or ASTM

standard incorporated by reference in Sec.171.7 of this subchapter

applicable to the requalifier's activities. This information must be the

same as contained in the edition incorporated by reference in Sec.

171.7 of this subchapter.

(b) Requalification records. Daily records of visual inspection,

pressure test, and ultrasonic examination if permitted under a special

permit, as applicable, must be maintained by the person who performs the

requalification until either the expiration of the requalification

period or until the cylinder is again requalified, whichever occurs

first. A single date may be used for each test sheet, provided each test

on the sheet was conducted on that date. Ditto marks or a solid vertical

line may be used to indicate repetition of the preceding entry for the

following entries only: date; actual dimensions; manufacturer's name or

symbol, if present; owner's name or symbol, if present; and test

operator. Blank spaces may not be used to indicate repetition of a prior

entry. The records must include the following information:

(1) Calibration test records. For each test to demonstrate

calibration, the date; serial number of the calibrated cylinder;

calibration test pressure; total, elastic and permanent expansions; and

legible identification of test operator. The test operator must be able

to demonstrate that the results of the daily calibration verification

correspond to the hydrostatic tests performed on that day. The daily

verification of calibration(s) may be recorded on the same sheets as,

and with, test records for that date.

[[Page 1134]]

(2) Pressure test and visual inspection records. The date of

requalification; serial number; DOT specification or special permit

number; marked pressure; actual dimensions; manufacturer's name or

symbol; owner's name or symbol, if present; result of visual inspection;

actual test pressure; total, elastic and permanent expansions; percent

permanent expansion; disposition, with reason for any repeated test,

rejection or condemnation; and legible identification of test operator.

For each cylinder marked pursuant to Sec.173.302a(b)(5) of this

subchapter, the test sheet must indicate the method by which any average

or maximum wall stress was computed. Records must be kept for all

completed, as well as unsuccessful tests. The entry for a second test

after a failure to hold test pressure must indicate the date of the

earlier test.

(3) Wall stress. Calculations of average and maximum wall stress

pursuant to Sec.173.302a(b)(3) of this subchapter, if performed.

(4) Calibration certificates. The most recent certificate of

calibration must be maintained for each calibrated cylinder.

(c) Repair, rebuilding or reheat treatment records. (1) Records

covering welding or brazing repairs, rebuilding or reheat treating shall

be retained for a minimum of fifteen years by the approved facility.

(2) A record of rebuilding, in accordance with Sec.180.211(d),

must be completed for each cylinder rebuilt. The record must be clear,

legible, and contain the following information:

(i) Name and address of test facility, date of test report, and name

of original manufacturer;

(ii) Marks stamped on cylinder to include specification number,

service pressure, serial number, symbol of manufacturer, inspector's

mark, and other marks, if any;

(iii) Cylinder outside diameter and length in inches;

(iv) Rebuild process (welded, brazed, type seams, etc.);

(v) Description of assembly and any attachments replaced (e.g.,

neckrings, footrings);

(vi) Chemical analysis of material for the cylinder, including seat

and Code No., type of analysis (ladle, check), chemical components

(Carbon (C), Phosphorous (P), Sulfur (S), Silicon (Si), Manganese (Mn),

Nickel (Ni), Chromium (Cr), Molybdenum (Mo), Copper (Cu), Aluminum (Al),

Zinc (Zn)), material manufacturer, name of person performing the

analysis, results of physical tests of material for cylinder (yield

strength (psi), tensile strength (psi), elongation percentage (inches),

reduction in area percentage, weld bend, tensile bend, name of

inspector);

(vii) Results of proof pressure test on cylinder, including test

method, test pressure, total expansion, permanent expansion, elastic

expansion, percent permanent expansion (permanent expansion may not

exceed ten percent (10%) of total expansion), and volumetric capacity

(volumetric capacity of a rebuilt cylinder must be within <plus-

minus<ls-thn-eq>3% of the calculated capacity);

(viii) Each report must include the following certification

statement: ``I certify that this rebuilt cylinder is accurately

represented by the data above and conforms to all of the requirements in

Subchapter C of Chapter I of Title 49 of the Code of Federal

Regulations.''. The certification must be signed by the rebuild

technician and principal, officer, or partner of the rebuild facility.

[67 FR 51660, Aug. 8, 2002, as amended at 68 FR 24664, May 8, 2003; 70

FR 73166, Dec. 9, 2005; 71 FR 54398, Sept. 14, 2006; 72 FR 55697, Oct.

1, 2007]

[Code of Federal Regulations]

[Title 49, Volume 2]

[Revised as of October 1, 2007]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR180.352]

[Page 1136-1138]

TITLE 49--TRANSPORTATION

CHAPTER I--PIPELINE AND HAZARDOUS MATERIALS SAFETY ADMINISTRATION,

DEPARTMENT OF TRANSPORTATION

PART 180_CONTINUING QUALIFICATION AND MAINTENANCE OF PACKAGINGS--Table

of Contents

Subpart D_Qualification and Maintenance of IBCs

Sec. 180.352  Requirements for retest and inspection of IBCs.

(a) General. Each IBC constructed in accordance with a UN standard

for which a test or inspection specified in paragraphs (b)(1), (b)(2)

and (b)(3) of this section is required may not be filled and offered for

transportation or transported until the test or inspection has been

successfully completed. This paragraph does not apply to any IBC filled

prior to the test or inspection due date. The requirements in this

section do not apply to DOT 56 and 57 portable tanks.

(b) Test and inspections for metal, rigid plastic, and composite

IBCs. Each IBC is subject to the following test and inspections:

(1) Each IBC intended to contain solids that are loaded or

discharged under pressure or intended to contain liquids must be tested

in accordance with the leakproofness test prescribed in Sec.178.813 of

this subchapter prior to its first use in transportation and every 2.5

years thereafter, starting from the date of manufacture or the date of a

repair conforming to paragraph (d)(1) of this section. For this test,

the IBC is not required to have its closures fitted.

(2) An external visual inspection must be conducted initially after

production and every 2.5 years starting from the date of manufacture or

the date of a repair conforming to paragraph (d)(1) of this section to

ensure that:

[[Page 1137]]

(i) The IBC is marked in accordance with requirements in Sec.

178.703 of this subchapter. Missing or damaged markings, or markings

difficult to read must be restored or returned to original condition.

(ii) Service equipment is fully functional and free from damage

which may cause failure. Missing, broken, or damaged parts must be

repaired or replaced.

(iii) The IBC is capable of withstanding the applicable design

qualification tests. The IBC must be externally inspected for cracks,

warpage, corrosion or any other damage which might render the IBC unsafe

for transportation. An IBC found with such defects must be removed from

service or repaired in accordance with paragraph (d) of this section.

The inner receptacle of a composite IBC must be removed from the outer

IBC body for inspection unless the inner receptacle is bonded to the

outer body or unless the outer body is constructed in such a way (e.g.,

a welded or riveted cage) that removal of the inner receptacle is not

possible without impairing the integrity of the outer body. Defective

inner receptacles must be replaced in accordance with paragraph (d) of

this section or the entire IBC must be removed from service. For metal

IBCs, thermal insulation must be removed to the extent necessary for

proper examination of the IBC body.

(3) Each metal, rigid plastic and composite IBC must be internally

inspected at least every five years to ensure that the IBC is free from

damage and to ensure that the IBC is capable of withstanding the

applicable design qualification tests.

(i) The IBC must be internally inspected for cracks, warpage, and

corrosion or any other defect that might render the IBC unsafe for

transportation. An IBC found with such defects must be removed from

hazardous materials service until restored to the original design type

of the IBC.

(ii) Metal IBCs must be inspected to ensure the minimum wall

thickness requirements in Sec.178.705(c)(1)(iv) of this subchapter are

met. Metal IBCs not conforming to minimum wall thickness requirements

must be removed from hazardous materials service.

(c) Visual inspection for flexible, fiberboard, or wooden IBCs. Each

IBC must be visually inspected prior to first use and permitted reuse,

by the person who places hazardous materials in the IBC, to ensure that:

(1) The IBC is marked in accordance with requirements in Sec.

178.703 of this subchapter. Additional marking allowed for each design

type may be present. Required markings that are missing, damaged or

difficult to read must be restored or returned to original condition.

(2) Proper construction and design specifications have been met.

(i) Each flexible IBC must be inspected to ensure that:

(A) Lifting straps if used, are securely fastened to the IBC in

accordance with the design type.

(B) Seams are free from defects in stitching, heat sealing or gluing

which would render the IBC unsafe for transportation of hazardous

materials. All stitched seam-ends must be secure.

(C) Fabric used to construct the IBC is free from cuts, tears and

punctures. Additionally, fabric must be free from scoring which may

render the IBC unsafe for transport.

(ii) Each fiberboard IBC must be inspected to ensure that:

(A) Fluting or corrugated fiberboard is firmly glued to facings.

(B) Seams are creased and free from scoring, cuts, and scratches.

(C) Joints are appropriately overlapped and glued, stitched, taped

or stapled as prescribed by the design. Where staples are used, the

joints must be inspected for protruding staple-ends which could puncture

or abrade the inner liner. All such ends must be protected before the

IBC is authorized for hazardous materials service.

(iii) Each wooden IBC must be inspected to ensure that:

(A) End joints are secured in the manner prescribed by the design.

(B) IBC walls are free from defects in wood. Inner protrusions which

could puncture or abrade the liner must be covered.

(d) Requirements applicable to repair of IBCs. (1) Except for

flexible and fiberboard IBCs and the bodies of rigid plastic and

composite IBCs, damaged IBCs

[[Page 1138]]

may be repaired and the inner receptacles of composite packagings may be

replaced and returned to service provided:

(i) The repaired IBC conforms to the original design type, is

capable of withstanding the applicable design qualification tests, and

is retested and inspected in accordance with the applicable requirements

of this section;

(ii) An IBC intended to contain liquids or solids that are loaded or

discharged under pressure is subjected to a leakproofness test as

specified in Sec.178.813 of this subchapter and is marked with the

date of the test; and

(iii) The IBC is subjected to the internal and external inspection

requirements as specified in paragraph (b) of this section.

(iv) The person performing the tests and inspections after the

repair must durably mark the IBC near the manfacturer's UN design type

marking to show the following:

(A) The country in which the tests and inspections were performed;

(B) The name or authorized symbol of the person performing the tests

and inspections; and

(C) The date (month, year) of the tests and inspections.

(v) Retests and inspections performed in accordance with paragraphs

(d)(1)(i) and (ii) of this section may be used to satisfy the

requirements for the 2.5 and five year periodic tests and inspections

required by paragraph (b) of this section, as applicable.

(2) Except for flexible and fiberboard IBCs, the structural

equipment of an IBC may be repaired and returned to service provided:

(i) The repaired IBC conforms to the original design type and is

capable of withstanding the applicable design qualification tests; and

(ii) The IBC is subjected to the internal and external inspection

requirements as specified in paragraph (b) of this section.

(3) Service equipment may be replaced provided:

(i) The repaired IBC conforms to the original design type and is

capable of withstanding the applicable design qualification tests;

(ii) The IBC is subjected to the external visual inspection

requirements as specified in paragraph (b) of this section; and

(iii) The proper functioning and leak tightness of the service

equipment, if applicable, is verified.

(e) Requirements applicable to routine maintenance of IBCs. Except

for routine maintenance of metal, rigid plastics and composite IBCs

performed by the owner of the IBC, whose State and name or authorized

symbol is durably marked on the IBC, the party performing the routine

maintenance shall durably mark the IBC near the manufacturer's UN design

type marking to show the following:

(1) The country in which the routine maintenance was carried out;

and

(2) The name or authorized symbol of the party performing the

routine maintenance.

(f) Retest date. The date of the most recent periodic retest must be

marked as provided in Sec.178.703(b) of this subchapter.

(g) Record retention. (1) The owner or lessee of the IBC must keep

records of periodic retests, initial and periodic inspections, and tests

performed on the IBC if it has been repaired or remanufactured.

(2) Records must include design types and packaging specifications,

test and inspection dates, name and address of test and inspection

facilities, names or name of any persons conducting test or inspections,

and test or inspection specifics and results.

(3) Records must be kept for each packaging at each location where

periodic tests are conducted, until such tests are successfully

performed again or for at least 2.5 years from the date of the last

test. These records must be made available for inspection by a

representative of the Department on request.

[Amdt. 180-5, 59 FR 38079, July 26, 1994, as amended at 64 FR 10782,

Mar. 5, 1999; 65 FR 58632, Sept. 29, 2000; 66 FR 45186, 45391, Aug. 28,

2001; 68 FR 45042, July 31, 2003; 69 FR 76186, Dec. 20, 2004; 70 FR

34399, June 14, 2005; 70 FR 56099, Sept. 23, 2005; 71 FR 78635, Dec. 29,

2006]

[[Page 1139]]