Bauer B Timer

Usage Clarification and Limitations

Only for use with Bauer Filter types – P21, P31, P41, 999xxx

For High Pressure Compressors Working at 200 or 300 bars

Part numbers	Description

57679		P21 Triplex MS/AC/MS

59183		P21 Triplex AC/MS/MS/HP with Hopcalite for CO removal

80100		P31 Cartridge MS/AC/MS

80114		P31 Cartridge AC/MS/MS/HP with Hopcalite for CO removal

82545		P31 Paintball Filter Cartridge MS only, not breathing air

82546		P21 Paintball Filter Cartridge MS only, not breathing air

62565		P41 Cartridge MS/AC/MS

67224		P41 Cartridge AC/MS/MS/HP with Hopcalite for CO removal

999xxx	Special Bauer Filter – Constituents not specified

| Filter Molecular Sieve Weights |  |  |  |  |
| --- | --- | --- | --- | --- |
| Bauer Filter Pn#/housing Pn# | Molecular sieve | weight | Activated Carbon |
| P21 #57679 / # 077159-EU | 80 | gram | 20 | gram |
| P31 #80100 / # 79873-EU |  | 300 | gram | 40 | gram |
| P41 #62565 / # 61685-EU |  | 600 | gram | 80 | gram(estimate) |
| P61 #58826 / # |  | 1000 | gram | 120 | gram(estimate) |

| Model | Nominal pressure | Flow rate at 200 bar 3000 psig |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| P40 | 90-420 bar 1300-6000 psig | 450 l/min 15 Scfm |  |  |  |  |  |  |  |
| P60 | 90-420 bar 1300-6000 psig | 600 l/min 20 Scfm |  |  |  |  |  |  |  |