[Code of Federal Regulations]

[Title 49, Volume 2, Parts 100 to 185]

[Revised as of October 1, 1999]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR178.2]

[Page 720]

TITLE 49--TRANSPORTATION

CHAPTER I--RESEARCH AND SPECIAL PROGRAMS ADMINISTRATION, DEPARTMENT OF

TRANSPORTATION

PART 178--SPECIFICATIONS FOR PACKAGINGS--Table of Contents

Sec. 178.2  Applicability and responsibility.

(a) Applicability. (1) The requirements of this part apply to

packagings manufactured--

(i) To a DOT specification, regardless of country of manufacture; or

(ii) To a UN standard, for packagings manufactured within the United

States. For UN standard packagings manufactured outside the United

States, see Sec. 173.24(d)(2) of this subchapter. For UN standard

packagings for which standards are not prescribed in this part, see

Sec. 178.3(b).

(2) A manufacturer of a packaging subject to the requirements of

this part is primarily responsible for compliance with the requirements

of this part. However, any person who performs a function prescribed in

this part shall perform that function in accordance with this part.

(b) Specification markings. When this part requires that a packaging

be marked with a DOT specification or UN standard marking, marking of

the packaging with the appropriate DOT or UN markings is the

certification that--

(1) Except as otherwise provided in this section, all requirements

of the DOT specification or UN standard, including performance tests,

are met; and

(2) All functions performed by, or on behalf of, the person whose

name or symbol appears as part of the marking conform to requirements

specified in this part.

(c) Notification. Except as specifically provided in Secs. 178.337-

18 and 178.345-10 of this part, the manufacturer or other person

certifying compliance with the requirements of this part, and each

subsequent distributor of that packaging shall--

(1) Notify in writing each person to whom that packaging is

transferred--

(i) Of all requirements in this part not met at the time of

transfer, and

(ii) Of the type and dimensions of any closures, including gaskets,

needed to satisfy performance test requirements.

(2) Retain copies of each written notification for at least one year

from date of issuance; and

(3) Make copies of all written notifications available for

inspection by a representative of the Department.

(d) Except as provided in paragraph (c) of this section, a packaging

not conforming to the applicable specifications or standards in this

part may not be marked to indicate such conformance.

(e) Definitions. For the purpose of this part--

Manufacturer means the person whose name and address or symbol

appears as part of the specification markings required by this part or,

for a packaging marked with the symbol of an approval agency, the person

on whose behalf the approval agency certifies the packaging.

Specification markings mean the packaging identification markings

required by this part including, where applicable, the name and address

or symbol of the packaging manufacturer or approval agency.

(f) No packaging may be manufactured or marked to a packaging

specification that was in effect on September 30, 1991, and that was

removed from this part 178 by a rule published in the Federal Register

on December 21, 1990 and effective October 1, 1991.

[Amdt. 178-97, 55 FR 52715, Dec. 21, 1990; 56 FR 66284, Dec. 20, 1991,

as amended by Amdt. No. 178-106, 59 FR 67519, Dec. 29, 1994; Amdt. 178-

117, 62 FR 14338, Mar. 26, 1997]

[Code of Federal Regulations]

[Title 49, Volume 2, Parts 100 to 185]

[Revised as of October 1, 1999]

From the U.S. Government Printing Office via GPO Access

[CITE: 49CFR178.46]

[Page 745-750]

TITLE 49--TRANSPORTATION

CHAPTER I--RESEARCH AND SPECIAL PROGRAMS ADMINISTRATION, DEPARTMENT OF

TRANSPORTATION

PART 178--SPECIFICATIONS FOR PACKAGINGS--Table of Contents

Subpart C--Specifications for Cylinders

Sec. 178.46  Specification 3AL seamless aluminum cylinders.

(a) Size and service pressure. A DOT 3AL cylinder is a seamless  aluminum cylinder with a maximum water capacity of 1000 pounds and  minimum service pressure of 150 psig.

(b) Authorized material and identification of material. The material of construction must meet the following conditions:

(1) Starting stock must be cast stock or traceable to cast stock.

(2) Material with seams, cracks, laminations, or other defects likely to weaken the finished cylinder may not be used.

(3) Material must be identified by a suitable method that will identify the alloy, the aluminum producer's cast number, the solution heat treat batch number and the lot number.

(4) The material must be of uniform quality. Only the following heat treatable aluminum alloys in table 1 and 2 are permitted as follows:

[[Page 746]]

Table 1--Chemical Composition Limits

[Chemical composition (in weight percent)]

--------------------------------------------------------------------------------------------------------------------------------------------------------

Other \1\

Aluminum Assoc. alloy           Si       Fe       Cu         Mn         Mg         Cr       Zn     Ti     Pb     Bi  --------------        A1

designation No.                                                                                                     Each  Total

--------------------------------------------------------------------------------------------------------------------------------------------------------

6351...........................    0.7-1.3   0.50       0.10  0.40-0.80  0.40-0.80  .........   0.20   0.20   0.01   0.01   0.05   0.15  Remainder.

6061...........................  0.40-0.80   0.70  0.15-0.40       0.15  0.80-1.20  0.04-0.35   0.25   0.15   0.01   0.01   0.05   0.15  Remainder.

--------------------------------------------------------------------------------------------------------------------------------------------------------

\1\ Analysis is regularly made only for the elements for which specific limits are shown, except for unalloyed aluminum. If, however, the presence of

other elements is suspected to be, or in the course of routine analysis is indicated to be in excess of specified limits, further analysis is made to

determine that these other elements are not in excess of the amounts specified. (Aluminum Association Standards and Data.)

[[Page 747]]

Table 2--Mechanical Property Limits

----------------------------------------------------------------------------------------------------------------

Tensile strength--PSI          Elongation--percent

----------------------------------------  minimum for 2" or

Alloy and temper                                                               4D \1\ size

Ultimate--minimum    Yield--minimum          specimen

----------------------------------------------------------------------------------------------------------------

6351-T6............................................              42,000              37,000                \2\14

6061-T6............................................              38,000              35,000                \2\14

----------------------------------------------------------------------------------------------------------------

\1\ ``D'' represents specimen diameters. When the cylinder wall is greater than \3/16\ inch thick, a retest

without reheat treatment using the 4D size specimen is authorized if the test using the 2 inch size specimen

fails to meet elongation requirements.

\2\ When cylinder wall is not over \3/16\-inch thick, 10 percent elongation is authorized when using a 24t x 6t

size test specimen.

(5) All starting stock must be 100 percent ultrasonically inspected,

along the length at right angles to the central axis from two positions

at 90 deg. to one another. The equipment and continuous scanning

procedure must be capable of detecting and rejecting internal defects

such as cracks which have an ultrasonic response greater than that of a

calibration block with a \5/64\-inch diameter flat bottomed hole.

(6) Cast stock must have uniform equiaxed grain structure not to

exceed 500 microns maximum.

(7) Any starting stock not complying with the provisions of

paragraphs (b)(1) through (b)(6) of this section must be rejected.

(c) Manufacture. Cylinders must be manufactured in accordance with

the following requirements:

(1) Cylinder shells must be manufactured by the backward extrusion

method and have a cleanliness level adequate to ensure proper

inspection. No fissure or other defect is acceptable that is likely to

weaken the finished cylinder below the design strength requirements. A

reasonably smooth and uniform surface finish is required. If not

originally free from such defects, the surface may be machined or

otherwise conditioned to eliminate these defects.

(2) Thickness of the cylinder base may not be less than the

prescribed minimum wall thickness of the cylindrical shell. The cylinder

base must have a basic torispherical, hemispherical, or ellipsoidal

interior base configuration where the dish radius is no greater than 1.2

times the inside diameter of the shell. The knuckle radius may not be

less than 12 percent of the inside diameter of the shell. The interior

base contour may deviate from the true torispherical, hemispherical or

ellipsoidal configuration provided that--

(i) Any areas of deviation are accompanied by an increase in base

thickness;

(ii) All radii of merging surfaces are equal to or greater than the

knuckle radius;

(iii) Each design has been qualified by successfully passing the

cycling tests in this paragraph (c); and

(iv) Detailed specifications of the base design are available to the

inspector.

(3) For free standing cylinders, the base thickness must be at least

two times the minimum wall thickness along the line of contact between

the cylinder base and the floor when the cylinders are in the vertical

position.

(4) Welding or brazing is prohibited.

(5) Each new design and any significant change to any acceptable

design must be qualified for production by testing prototype samples as

follows:

(i) Three samples must be subjected to 100,000 pressure reversal

cycles between zero and service pressure or 10,000 pressure reversal

cycles between zero and test pressure, at a rate not in excess of 10

cycles per minute without failure.

(ii) Three samples must be pressurized to destruction and failure

may not occur at less than 2.5 times the marked cylinder service

pressure. Each cylinder must remain in one piece. Failure must initiate

in the cylinder sidewall in a longitudinal direction. Rate of

pressurization may not exceed 200 psi per second.

(6) In this specification ``significant change'' means a 10 percent

or greater change in cylinder wall thickness, service pressure, or

diameter; a 30 percent or greater change in water capacity or base

thickness; any change in material; over 100 percent increase in size of

openings; or any change in the number of openings.

[[Page 748]]

(d) Wall thickness. The minimum wall thickness must be such that the

wall stress at the minimum specified test pressure will not exceed 80

percent of the minimum yield strength nor exceed 67 percent of the

minimum ultimate tensile strength as verified by physical tests in

paragraph (i) of this section. The minimum wall thickness for any

cylinder with an outside diameter greater than 5 inches must be 0.125

inch. Calculations must be made by the following formula:

S = [P(1.3D\2\ + 0.4d\2\)] / (D\2\ - d\2\)

Where:

S = Wall stress in pounds per square inch;

P = Prescribed minimum test pressure in pounds per square inch (see

paragraph (g) of this section);

D = Outside diameter in inches; and

d = Inside diameter in inches.

(e) Openings. Openings must comply with the following requirements:

(1) Openings are permitted in heads only.

(2) The size of any centered opening in a head may not exceed one-

half the outside diameter of the cylinder.

(3) Other openings are permitted in the head of a cylinder if:

(i) Each opening does not exceed 2.625 inches in diameter, or one-

half the outside diameter of the cylinder; whichever is less;

(ii) Each opening is separated from each other by a ligament; and

(iii) Each ligament which separates two openings must be at least

three times the average of the diameters of the two openings.

(4) All openings must be circular.

(5) All openings must be threaded. Threads must comply with the

following:

(i) Each thread must be clean cut, even, without checks, and to

gauge.

(ii) Taper threads, when used, must conform to one of the following:

(A) American Standard Pipe Thread (NPT) type, conforming to the

requirements of Federal Standard H-28, Section 7;

(B) National Gas Taper Thread (NGT) type, conforming to the

requirements of Federal Standard H-28, Sections 7 and 9; or

(C) Other taper threads conforming to other standards may be used

provided the length is not less than that specified for NPT threads.

(iii) Straight threads, when used, must conform to one of the

following:

(A) National Gas Straight Thread (NGS) type, conforming to the

requirements of Federal Standard H-28, Sections 7 and 9;

(B) Unified Thread (UN) type, conforming to the requirements of

Federal Standard H-28, Section 2;

(C) Controlled Radius Root Thread (UN) type, conforming to the

requirements of Federal Standard H-28, Section 4; or

(D) Other straight threads conforming to other recognized standards

may be used provided that the requirements in paragraph (e)(5)(iv) of

this section are met.

(iv) All straight threads must have at least 6 engaged threads, a

tight fit, and a factor of safety in shear of at least 10 at the test

pressure of the cylinder. Shear stress must be calculated by using the

appropriate thread shear area in accordance with Federal Standard H-28,

Appendix A5, Section 3.

(f) Heat treatment. Prior to any test, all cylinders must be

subjected to a solution heat treatment and aging treatment appropriate

for the aluminum alloy used.

(g) Hydrostatic test. Each cylinder must be subjected to an internal

test pressure using the water jacket equipment and method or other

suitable equipment and method and comply with the following

requirements:

(1) The testing apparatus must be operated in a manner so as to

obtain accurate data. The pressure gauge used must permit reading to an

accuracy of one percent. The expansion gauge must permit reading the

total expansion to an accuracy of either one percent or 0.1 cubic

centimeter.

(2) The test pressure must be maintained for a sufficient period of

time to assure complete expansion of the cylinder. In no case may the

pressure be held less than 30 seconds. If, due to failure of the test

apparatus, the required test pressure cannot be maintained, the test may

be repeated at a pressure increased by 10 percent or 100 psi, whichever

is lower. If the test apparatus again fails to maintain the test

pressure, the cylinder being tested

[[Page 749]]

must be rejected. Any internal pressure applied to the cylinder before

any official test may not exceed 90 percent of the test pressure.

(3) The minimum test pressure is the greatest of the following:

(i) 450 psi regardless of service pressure;

(ii) Two times the service pressure for cylinders having service

pressure less than 500 psi; or

(iii) Five-thirds times the service pressure for cylinders having a

service pressure of at least 500 psi.

(4) Permanent volumetric expansion may not exceed 10 percent of

total volumetric expansion at test pressure.

(h) Flattening test. One cylinder taken at random out of each lot

must be subjected to a flattening test as follows:

(1) The test must be between knife edges, wedge shaped, having a

60 deg. included angle, and rounded in accordance with the following

table. The longitudinal axis of the cylinder must be at an angle 90 deg.

to the knife edges during the test. The flattening test table is as

follows:

Table 3--Flattening Test Table

------------------------------------------------------------------------

Radius

Cylinder wall thickness in inches                   in

inches

------------------------------------------------------------------------

Under .150....................................................      .500

.150 to .249..................................................      .875

.250 to .349..................................................     1.500

.350 to .449..................................................     2.125

.450 to .549..................................................     2.750

.550 to .649..................................................     3.500

.650 to .749..................................................     4.125

------------------------------------------------------------------------

(2) An alternate bend test in accordance with ASTM E 290 using a

mandrel diameter not more than 6 times the wall thickness is authorized

to qualify lots that fail the flattening test of this section without

reheat treatment. If used, this test must be performed on two samples

from one cylinder taken at random out of each lot of 200 cylinders or

less.

(3) Each test cylinder must withstand flattening to nine times the

wall thickness without cracking. When the alternate bend test is used,

the test specimens must remain uncracked when bent inward around a

mandrel in the direction of curvature of the cylinder wall until the

interior edges are at a distance apart not greater than the diameter of

the mandrel.

(i) Mechanical properties test. Two test specimens cut from one

cylinder representing each lot of 200 cylinders or less must be

subjected to the mechanical properties test, as follows:

(1) The results of the test must conform to at least the minimum

acceptable mechanical property limits for aluminum alloys as specified

in paragraph (b) of this section.

(2) Specimens must be 4D bar or gauge length 2 inches with width not

over 1\1/2\ inch taken in the direction of extrusion approximately

180 deg. from each other; provided that gauge length at least 24 times

thickness with width not over 6 times thickness is authorized, when

cylinder wall is not over \3/16\ inch thick. The specimen, exclusive of

grip ends, may not be flattened. Grip ends may be flattened to within

one inch of each end of the reduced section. When the size of the

cylinder does not permit securing straight specimens, the specimens may

be taken in any location or direction and may be straightened or

flattened cold by pressure only, not by blows. When such specimens are

used, the inspector's report must show that the specimens were so taken

and prepared. Heating of specimens for any purpose is forbidden.

(3) The yield strength in tension must be the stress corresponding

to a permanent strain of 0.2 percent of the gauge length.

(i) The yield strength must be determined by either the ``offset''

method or the ``extension under load'' method as prescribed in ASTM

Standard B-557.

(ii) In using the ``extension under load'' method, the total strain

(or ``extension under load'') corresponding to the stress at which the

0.2 percent permanent strain occurs may be determined with sufficient

accuracy by calculating the elastic extension of the gauge length under

appropriate load and adding thereto 0.2 percent of the gauge length.

Elastic extension calculations must be based on an elastic modulus of

10,000,000 psi. In the event of controversy, the entire stress-strain

diagram must be plotted and the yield strength determined from the 0.2

percent offset.

(iii) For the purpose of strain measurement, the initial strain must

be set while the specimen is under a stress of

[[Page 750]]

6,000 psi, the strain indicator reading being set at the calculated

corresponding strain.

(iv) Cross-head speed of the testing machine may not exceed \1/8\

inch per minute during yield strength determination.

(j) Rejected cylinder. Reheat treatment of rejected cylinders is

authorized one time. Subsequent thereto, cylinders must pass all

prescribed tests to be acceptable.

(k) Duties of inspector. In addition to the requirements of

Sec. 178.35, the inspector shall:

(1) Verify compliance with the provisions of paragraph (b) of this

section by:

(i) Performing or witnessing the performance of the chemical

analyses on each melt or cast lot or other unit of starting material; or

(ii) Obtaining a certified chemical analysis from the material or

cylinder manufacturer for each melt, or cast of material; or

(iii) Obtaining a certified check analysis on one cylinder out of

each lot of 200 cylinders or less, if a certificate containing data to

indicate compliance with the material specification is obtained.

(2) The inspector shall verify ultrasonic inspection of all material

by inspection or by obtaining the material producer's certificate of

ultrasonic inspection. Ultrasonic inspection must be performed or

verified as having been performed in accordance with paragraph (c) of

this section.

(3) The inspector must also determine that each cylinder complies

with this specification by:

(i) Selecting the samples for check analyses performed by other than

the material producer;

(ii) Verifying that the prescribed minimum thickness was met by

measuring or witnessing the measurement of the wall thickness; and

(iii) Verifying that the identification of material is proper.

(4) Prior to initial production of any design or design change,

verify that the design qualification tests prescribed in paragraph

(c)(6) of this section have been performed with acceptable results.

(l) Definitions. (1) In this specification, a ``lot'' means a group

of cylinders successively produced having the same:

(i) Size and configuration;

(ii) Specified material of construction;

(iii) Process of manufacture and heat treatment;

(iv) Equipment of manufacture and heat treatment; and

(v) Conditions of time, temperature and atmosphere during heat

treatment.

(2) In no case may the lot size exceed 200 cylinders, but any

cylinder processed for use in the required destructive physical testing

need not be counted as being one of the 200.

(m) Inspector's report. In addition to the information required by

Sec. 178.35, the record of chemical analyses must also include the alloy

designation, and applicable information on iron, titanium, zinc,

magnesium and any other applicable element used in the construction of

the cylinder.