Maintenance schedule / check interval AANX 500

# Carry out maintenance to the following schedule

# Check operating hours on the hour counter and follow the instructions below

Screw Compressor

| Maintenance intervals (OH = Operating hours) | Maintenance |
| --- | --- |
| before putting into operation | check oil level check tension of drive belt check rotation of the compressor!! |
| after first 25 OH | check tension of the drive belt and oil level |
| After first 50 OH | check oil level change oil filter tighten up all pipe joints and electrical connections check all screwed connections for tightness check tension of the drive belt check alignment of the drive belt reseal pipe connections as necessary |
| each 100 OH | check oil level, operating pressure and temperature (combistat) check written maintenance schedule (optional) check tension of the drive belt check the intake filter for contamination |
| each 500 OH | change oil filter change oil clean / change air filter change separator cartridge check and adjust the final pressure setting if necessary tighten all electrical connections check tension of drive belt, if necessary change or re-tension clean oil cooler take off and clean oil return glass ( if existing ) check for leaks at gasket seals check run on time of 3 minutes. It must not be less than 3 minutes check bearings in drive belt tensioner, if necessary change it |

Nitrox Generator

| Maintenance intervals (OH = Operating hours) | Maintenance |
| --- | --- |
| before putting into operation | tighten up all pipe joints and electrical connections check for leaks at gasket seals and pipes check refrigeration dryer of operation |
| each 100 OH | check for leaks at gasket seals and pipes check and calibrate oxygen analyzer check refrigeration dryer |
| each 250 OH (at least every 12 months) | change all 3 filters (Blue Colour) clean / change air filter tighten all electrical connections check for leaks at gasket seals and pipes clean the enclosure adjust regulator |
| each 1000 OH (at least every 12 months) | change oxygen sensor check membrane performance |

General comments regarding maintenance

# Follow all safety precautions and take care during maintenance.

- Maintenance must be carried out under the supervision of authorised persons

- Use only suitable tools for maintenance

- Use only original parts

- Only carry out maintenance with the motor off and with the electricity supply isolated. Prevent the compressor being started by third parties

- Let the compressor cool down before maintenance, otherwise there would be the danger of being burned. Only for oil change should the compressor be warm; follow instructions.

- Before removing parts which could be under pressure, close the outlet valve and let the compressor vent completely.

- Keep all parts clean during maintenance, cover all parts with paper, foil or clean cloth.

- Protect motor, air-filter, electrical components etc. against humidity, e.g. during cleaning

- Don’t weld close to the oil-system. Empty and clear the oil tank before doing such work.

- Do not let any tools, cloth or loose parts fall into the compressor

- After maintenance check pressure, temperature and time settings before releasing the compressor back into use, check regulators and the stop button!

- Close the doors of the compressor before starting, even for a trial run!

- Do not change or remove soundproof material.

Maintenance Parts

Screw Compressor

| Qty. | Description | Articel No.: | Interval |
| --- | --- | --- | --- |
| 1 | Air Filter | R-8556 | 500hr |
| 1 | Oil Filter | R-333 | 500hr |
| 1 | Separator Cartridge | R-12101 | 500hr |
| 1 | Belt Tensioner Bearing | 2x6204 | 6000hr |
| 1 | Compressor Oil 10 liter | D68 | 500hr |
| 1 | V-Belt Set 3x | 101700 | 6000hr |

Nitrogen Generator AANX - 550

| Qty. | Description | Articel No.: | Interval |
| --- | --- | --- | --- |
| 1 | Filter (Blue colour) | EA30 | 250hr |
| 1 | Oxygen Sensor | GR-O2 | 1000hr/1year |